## Slide 1: Intelligent Data Visualization for Cross-Checking Spacecraft System Diagnoses
Presented at: AIAA Infotech@Aerospace 2012
Culver City, CA
June 21, 2012
Authors: Jim Ong, Emilio Remolina, David Breeden,
Brett Stroozas, John L Mohammed
Project sponsor: NASA

## Slide 2: Project Overview
Motivation
Project Goal
Future space missions will require automated system management.
Diagnostic reasoning systems are fallible when problems lie outside its expertise.
Cross-checking enables crew to consider alternate diagnoses and analyze evidence.
Cross-checking improves diagnostic accuracy and increases trust in automation.
Develop intelligent data visualization software that helps users cross-check automated diagnostic reasoning systems more quickly and accurately.
Notes: Jim 1

## Slide 3: Test Data: Diagnosis Competition (DxC 09)
ADAPT Testbed
Diagnostic Algorithms (DAs)
Sensor data
Injected faults
Commands
DA Diagnoses
Intelliviz
Notes: Jim 1

## Slide 4: DxC: ADAPT Electrical System Testbed
Notes: Jim 1

## Slide 5: Intelliviz Development Process
Manually Cross-Checked Diagnoses
Developed Baseline Data Viz Software
Identified Cross-Checking
Strategies and Heuristics
Developed Intelligent Diagnostic Assistance
Enhanced Analyses and Visualizations
Notes: Jim 1

## Slide 6: DxC: Exp #824 Diagnoses, Symptom
Auto Dx = Fan
Alt Dx = Fan Speed Sensor
Alt Dx = Relay
Notes: Jim 1

## Slide 7: Initial Time-Oriented Data Display
Notes:   No comments

## Slide 8: DxC: Cross-Checking Heuristics
Prioritize diagnoses and cross-checking
Identify symptoms underlying diagnosis
Assess plausibility of symptoms
Recognize sensor reading signatures.
Understand the reasoning behind the original diagnosis.
Hypothesize and evaluate alternate diagnoses.
Understand the overall pattern of problems and events.
Look for abrupt changes
Consider earlier events if necessary.
Notes: Jim 1

## Slide 9: DxC: Cross-Checking Heuristics (2)
Search for components that might cause a component to misbehave.
Search for possible causes that are near the symptoms.
Check other sensor data for consistency with candidate fault.
When explaining symptoms, consider specific failure modes.
Divide and conquer
Compare component’s behavior with reference values and relationships.
Compare component’s behavior with a similar component’s.
Exploit physical constraints.
Notes: Jim 1

## Slide 10: DxC: Interactive Analysis, Visualization
Automated Data Change Detection
Filter Data By:
Color-coded schematic
Detect and highlight abrupt changes in value, slope, variation
Change in value, slope, variation
Location w/rt selected component (upstream, downstream, sibling, cousin)
User-specified distance
Sensor type: current, voltage, etc.
Shows spatial patterns of sensors that satisfy filter criteria
Notes: Jim 1

## Slide 11: Automated Change Detection
Automatically detected changes
Sensor selected in schematic
Notes:   No comments

## Slide 12: ADAPT Interactive Schematic Display
Color-coding highlights selected components and sensors
Sensor selection criteria
Notes:   No comments

## Slide 13: Intelligent Data Visualization Assistant
Hypotheses, Data Patterns, Rationale
Pattern Detection
Spatial-Temporal Data Displays
Sensor Data
Data Visualization
Context
Rationale
Display

## Slide 14: Diagnostic Rules
DA Diagnosis
Symptom A
Symptom B
Diagnosis 2
Diagnosis 1
Data Pattern D
Data Pattern C
Symptom Rules
Find data patterns the original Dx might explain
Support Rules
Hypothesis Rules
Find patterns that support or rebut Dxs.
Find alternate Dxs that might explain a symptom
Notes:   No comments

## Slide 15: Example Symptom Rule
IF The DA Diagnosis is: a CIRCUIT-BREAKER failed in mode STUCK-CLOSED, and The following data pattern is present: There is a sensor of type CB-POSITION-SENSOR that is linked to the CIRCUIT-BREAKER and There is a data patterns for the sensor variable: EXISTS_VALUE CLOSED and The start time of the sensor data pattern precedes the hypothesis by less than 5 seconds. THEN assume that the DA diagnosis might have been generated to explain this data pattern (symptom).
Notes:   No comments

## Slide 16: Diagnostic Rationale Matrix
Notes:   No comments

## Slide 17: Intelliviz / Kepler Prototype
Notes: Jim 1.5

## Slide 18: ACAWS Eye Movement Data
Notes: Jim 1.5

## Slide 19: Results
Arrays of graphs and timelines (DataMontage), integrated with spatial data displays, are effective for analyzing complex, spatial-temporal data more effectively.
Simple diagnostic reasoning + data visualization accelerates diagnosis and cross-checking by helping users detect, review, and interpret relevant data patterns more quickly.
.
Notes: Jim 1

## Slide 20: Technologies
.
DataMontage
Intelligent Diagnosis
Cross-checking
Modular Java software for visualizing complex, time-oriented data (TRL 9)
Proof of concept prototype that detects and displays important data patterns to accelerate cross-checking and diagnosis (TRL 6)
Notes: Jim 1